Tseng Super VGA

    ET3000-AX   512k 8/16 bit Main chip
          -BX   512k  8 bit
          -Bp   256k  8 bit  Basic chip
    ET4000      1M 8/16 bit


    Registers:

       102h: Microchannel Setup Control
         bit 0  Disable Card if set

       3C0h index 16h: ATC Miscellaneous
         (Write data to 3C0h, Read from 3C1h  (May not be needed))
       bit 4,5  High resoloutionn timings.

       3C3h (R/W): Microchannel Video Subsystem Enable Register:
         bit 0  Enable Microchannel VGA if set

       3C4h index  6  (R/W): Zoom Control   (ET3000 Only)
       bit 0-2  Yzoom factor 0=1:1
           4-6  Xzoom factor 0=1:1
             7  Hardware zoom enabled if set

       3C4h index  7  (R/W): TS Auxiliary Mode
         bit 0  (ET3000 Only) Switch Normal Window if set (Text/Graph)
             1  (ET3000 Only) Switch Zoom Window if set (Text/Graph)
             2  (ET3000 Only) Switch Split Window if set (Text/Graph)
             4  (ET3000 Only) If set 8 simultaneous fonts are enabled,
                              using bit 3,4,6 of each attribute byte
                              to select the font.
           3,5  Rom Bios Enable/Disable:
                  0 0  C000-C3FF Enabled
                  0 1  Rom disabled
                  1 0  C000-C5FF,C680-C7FF Enabled
                  1 1  C000-C7FF Enabled
             6  MCLK/2 if set
             7  VGA compatible if set EGA else.

       3CBh (R/W): PEL Address/Data
  
       3CDh (R/W): Segment Select
       bit 0-2  (ET3000) 64k Write bank nr
           3-5  (ET3000) 64k Read bank nr
           6-7  (ET3000) Segment Configuration.
                           0  128K segments
                           1   64K segments
                           2  1M linear memory
           0-3  (ET4000) 64k Write bank nr (0..15)
           4-7  (ET4000) 64k Read bank nr (0..15)

       3d4h index 1Bh (R/W): X Zoom Start Address       (ET3000 Only)
       bit 0-7  Offset of Zoom window start in character clocks
                (8 pixels) from left edge

       3d4h index 1Ch (R/W): X Zoom End                 (ET3000 Only)
       bit 0-7  Offset of Zoom window end in char clocks from left edge

       3d4h index 1Dh (R/W): Y Zoom Start Address       (ET3000 Only)
       bit 0-7  Start line of zoom window bit 0-7

       3d4h index 1Eh (R/W): Y Zoom End Address         (ET3000 Only)
       bit 0-7  (ET3000 Only) End line of zoom window bit 0-7

       3d4h index 1Fh (R/W): Y Zoom Start and End High  (ET3000 Only)
       bit 0-2  End line of zoom window bit 8-10
           3-5  Start line of zoom window bit 8-10

       3d4h index 20h (R/W): Zoom Start Address Low     (ET3000 Only)
       bit 0-7  Zoom Start Address bit 0-7
                Adress of Zoom data

       3d4h index 21h (R/W): Zoom Start Address Middle  (ET3000 Only)
       bit 0-7  Zoom Start Address bit 8-15

       3d4h index 23h (R/W): Extended start ET3000      (ET3000 Only)
         bit 0  Cursor start adress bit 16
             1  Display start adress bit 16
             2  Zoom start adress bit 16

       3d4h index 24h (R/W): Compatability Control
         bit 0  Enable Clock Translate
             1  Additional Master Clock Select
             2  Enable tri-state for all output pins
             3  Enable input A8 of 1MB DRAMs
             4  Reserved
             5  Enable external ROM CRTC translation
             6  Enable Double Scan and Underline Attribute
             7  CGA/MDA/Hercules

       3d4h index 25h (R/W): Overflow High ET3000       (ET3000 Only)
         bit 0  Vertical Blank Start bit 10
             1  Vertical Total Start bit 10
             2  Vertical Display End bit 10
             3  Vertical Sync Start bit 10
             4  Line Compare bit 10
           5-6  Reserved
             7  Vertical Interlace if set

       3d4h index 32h (R/W): RAS/CAS Video Config
         Ram timing, System clock and Ram type. Sample values:
           00h  VRAM  80nsec
           09h  VRAM 100nsec
           00h  VRAM  28MHz
           08h  VRAM  36MHz
           70h  DRAM  40MHz

       3d4h index 33h (R/W): Extended start ET4000  (ET4000 Only)
       bit 0-1  Display start adress bits 16-17
           2-3  Cursor start adress bits 16-17
                Can be used to ID ET4000

       3d4h index 34h (R/W): Compatibility Control Register
         bit 3  if set Video Subsystem Enable Register at 46E8h
                  else at 3C3h.

       3d4h index 35h (R/W): Overflow High ET4000   (ET4000 Only)
         bit 0  Vertical Blank Start Bit 10
             1  Vertical Total Bit 10
             2  Vertical Display End Bit 10
             3  Vertical Sync Start Bit 10
             4  Line Compare Bit 10
             5  Gen-Lock Enabled if set (External sync)
             6  Read/Modify/Write Enabled if set
                Currently not implemented.
             7  Vertical interlace if set

       3d4h index 36h (R/W): Video System Configuration 1
         bit 3  16 bit wide fonts if set, else 8 bit wide
             4  (ET4000 Only) Linear adressing if set
                Video Memory is mapped as a 1 Meg block above 1MB.
             6  16 bit data path (video memory) if set
             7  16 bit data (I/O operations) if set

       3d4h index 37h (R/W): Video System Configuration 2
       bit 0-1  Memory size  0,1=256k, 2=512k, 3=1M   ???
             3  Clear if 64kx4 RAMs                   ???
                if set RAM size = (bit 0-1)*256k
                  else RAM size = (bit 0-1)* 64k

             4    16 bit ROM access if set
             5    Memory bandwidth (0 better than 1) ???
             7    VRAM installed if set DRAM else.
         bit 6?   Block read ahead (BRA)  if clear

      46E8h (R):  Video Subsystem Enable Register
         bit 3  Enable VGA if set


       3C4h index 05 used.
       3CBh used.   PEL Add/Dat. ??
       3CEh index 0Dh-0Eh used.


  Bank Switching:

     64k banks are selected by the Segment Select Register at 3CDh.
     Both a Read and a Write segment can be selected.

  Hardware Zoom (ET3000 Only).

     The ET3000 can zoom a part of display memory in a window.
     The display memory position and window position are selected
     by 3d4h index 1Bh to 21h.


  Identify Tseng Chipset:

     old:=port[$3CD];
     port[$3cd]:=$55;
     new:=port[$3cd];
     port[$3cd]:=old;

     if new=$55 then Tseng Chip !!!


  Identify Tseng 4000:

     if odd(port[$3cc]) then base:=$3d4 else base:=$3b4;

     port[base]:=$33;old_value:=port[base+1];
     new_value:=old_value xor 15;
     port[base+1]:=new_value;
     value:=port[base+1];
     port[base+1]:=old_value;

     if value=new_value then ET4000 chip !!!


  Video Modes:
     8   T   132   25   2                   (STB only)
     Ah  T   132   44   2

    18h  T   132   44   4  (8x8)   B000
    19h  T   132   25   4  (9x14)  B000
    1Ah  T   132   28   4  (9x13)  B000
    22h  T   132   44  16  (8x8)
    23h  T   132   25  16  (8x14)
    24h  T   132   28  16  (8x13)
    25h  G   640  480  16  planar
    26h  T    80   60  16  (8x8)
    27h  G   720  512  16  planar           (Tseng recomanded, few boards)
    29h  G   800  600  16  planar
    2Ah  T   100   40  16  planar
    2Dh  G   640  350 256  packed
    2Eh  G   640  480 256  packed
    2Fh  G   640  400 256  packed           (ET4000 Only)
    2Fh  G   720  512 256  packed           (Tseng recomanded, few boards)
    30h  G   800  600 256  packed
    36h  G   960  720  16  planar           (STB only)
    37h  G  1024  768  16  planar
    38h  G  1024  768 256  packed           (ET4000 Only)
    3Dh  G  1280 1024  16  planar           (newer ET4000s)




See Hicolor.doc for information about the Sierra HiColor RAMDAC.